Unless noted otherwise numbers are little-endian and 16-bit

Packet
command	param[5]
uint16	u?int16

0x8001	Travels the beam (move without cutting)
param0: y uint16
param1: x uint16
param3: distance

0x8002	no operation (use this to pad all packets to exactly 256 commands)

0x8004	Wait
param0: 1 unit = 10 microseconds

0x8005 Cut movement
param0: y uint16
param1: x uint16 “galvo units?”
param2: unknown, sometimes it is 0x0000, others 0x8000
Seems to be 0x0000 when it is the first movement of a
figure, or is part of raster or hatch, or goes straight.	0x8000 when it makes a sharp turn, 0x4000 when it makes a gentle turn; When cutting ovals, it is a small number instead. Probably related to ringing compensation.
param3: distance covered by this movement (must be calculated, or else it will not work.)

0x8006	Set traveling speed
param0: the speed, in units of ~1.9656 mm/sec
(probably affected by lens compensation/calibration)

0x8007	Laser On TC(us)
param0: microseconds (1:1)
0x8008	Laser Off TC(us)
param0: microseconds (1:1)

0x800C	Set cutting speed
param0: the speed,	in units of 1.9656 mm/sec
maybe affected by working area of installed lens?

0x800D	Often seen before cutting & between things, esp 0x8001
param0: 0x0008, 0x0007, 0x0006, 0x0000, 0x0001

0x800F	Unknown parameter setup
param0: 0x000A (usually), 0x0000 (sometimes...)

0x8012	Set laser power
90% = 3685; 50% = 2047; 33% = 1351
param0: 1 unit = 0.02443% (max=4095 presumably)

0x801B	Related to q switch frequency
param0 – period. 1 unit is 50 ns

0x8021	Laser state control
param0 – turn it on or off. 1=on. 0=off.

0x8051	Begins a job (can be used at the head of every packet if you like)
no parameters